## Slide 1
Micro Processors & Interfacing
16CS307
Mr. M Krishna Chennakesava Rao,
Asst. Professor, Dept. of ECE,
VFSTR University

## Slide 2
Micro Processor & Micro Controllers
Input
Device
MEMORY
CPU
Output
Device
Input
Device
MEMORY
Micro Processor
Output
Device
Schematic Diagram of Digital Computer
Schematic Diagram of Micro Computer
Ref: B Ram

## Slide 3
I / O
Ports
CPU
MEMORY
Input
Device
Output
Device
Control Bus
Control Bus
Data Bus
Address Bus
Block diagram of Micro Computer
Ref: Douglas V Hall

## Slide 4
ALU
Accumulator
General & Special Purpose Registers
Timing and Control Unit
Schematic Diagram / Internal parts of Micro Processor
Ref: B Ram

## Slide 5
UNIT 1 - Introduction to 8086 Microprocessor
UNIT 2 - Hardware features of 8086
UNIT 3 - Advanced Processors
UNIT 4 - Introduction to 8051Microcontroller
UNIT 5 - 8051 Microcontroller Hardware
Micro Processor & Micro Controllers
Syllabus Overview

## Slide 6
UNIT 1 - Introduction to 8086microprocessor
        History of Micro processors
        Architecture of 8086  Register model
        Memory Segmentation
        Software Aspects of 8086  Addressing modes
         Instruction set
         Interrupts  Hardware Interrupts
        Software Interrupts
UNIT 2 - Hardware features of 8086 :
        Pins
        Max / Min modes
        Memory Interfacing
Micro Processor & Micro Controllers
Syllabus Overview

## Slide 7
UNIT 3 - ADVANCED PROCESSORS
Real and Virtual Memory Addressing Modes
Memory Management
Memory Paging Mechanism
Cache Memory Techniques
Exception Handling
Comparison of Microprocessors (8086 – 80186 – 80286 – 80386 – 80486)
Comparison of Pentium Processors.
UNIT 4 - Introduction to 8051Microcontroller
    Comparison of Micro processor and micro controller
    8051 Architecture, Pin Diagram
    Software Aspects of 8051  Addressing modes
         Instruction set
         Simple programs
Micro Processor & Micro Controllers
Syllabus Overview

## Slide 8
UNIT 5 - 8051 Microcontroller Hardware :
Micro Processor & Micro Controllers
Syllabus Overview
ParallelPortsin8051, 8051Serialports
ExternalMemoryinterfacingwith8051,
8051Timers,
8051 Interrupts.
LCD & Keyboard Interfacing
ADC & DAC Interfacing
Stepper Motor Interfacing
External Memory interfacing.

## Slide 9
TEXTBOOKS :
Douglas V.Hall, “Microprocessors & Interfacing”, 2nd ed., TMH, 2003.
2. Kenneth J. Ayala, “8051 Microcontrollers”, Cengage Learning, 2008.
REFERENCEBOOKS :
1. A K Ray and KM Bhurchandi, “Advanced Microprocessors & Peripherals”, 2nd ed., TMH, 2006.
2. Raj Kamal, “Microcontroller architecture, programming, Interfacing and System Design”, Pearson Education, 2005
3. The 8051 Microcontroller and Embedded Systems using Assembly and C – Muhammad Ali Mazidi, J anice Gillispie Mazidi, Rolin D. McKinlay, 2nd Edn, Pearson Education, 2008.
4. Barry B.Brey: Intel Microprocessor Architecture, Programming and Interfacing- 8086/8088, 80186, 80286, 80386 and 80486,PHI,1995.

## Slide 10
UNIT - 1
Introduction to 8086 Micro Processor

## Slide 11
Evolution Of Microprocessors,
8086 Microprocessor, Architecture,
Register Model,
Memory Segmentation,
Physical Address Generation,
Addressing Modes,
Instruction Set,
Interrupts Of 8086,
Interrupt Vector Table.
Introduction to 8086 Micro Processor
Unit-1 Topics:

## Slide 12
Microprocessors can be defined based on 3 things. They are
Based on the application of the device.
The CPU of any microcomputer is called microprocessor.
ii. Based on the name of the device.
A small device which is able to do data processing is called microprocessor.
Based on the construction and operation of the device.
Microprocessor is a VLSI/ULSI chip.
It accepts binary data from either an i/p device or from the memory and
it access the instruction from the memory and it perform the operation of the
received data according to the instruction & produces the results those are sent to
either an o/p device or memory.
Definition of microprocessor:

## Slide 13
Evolution of Microprocessors
History of microprocessors: - Main parameter  word length
Definitions of word length: -
The no. of bits processed by the CPU at a time are called word length.
(or)
The no. of bits transmitted or received by the CPU at a time.
(or)
The no. of bits identified by the CPU at a time are called word length.

## Slide 14
First Generation
Between 1971 – 1973
PMOS technology, non compatible with TTL
4 bit processors  16 pins
8 and 16 bit processors  40 pins
Due to limitations of pins, signals are multiplexed
Intel 4004,4040 (4 bit processors)
Second Generation
During 1973
NMOS technology  Faster speed, Higher density, Compatible with TTL
4 / 8/ 16 bit processors  40 pins
Ability to address large memory spaces and I/O ports
Greater number of levels of subroutine nesting
Better interrupt handling capabilities
Intel 8085 (8 bit processor)
Third Generation
During 1978
HMOS technology  Faster speed, Higher packing density
16 bit processors  40/ 48/ 64 pins
Easier to program
Dynamically relatable programs
Processor has multiply/ divide arithmetic hardware
More powerful interrupt handling capabilities
Flexible I/O port addressing
Intel 8086 (16 bit processor)
Fourth Generation
During 1980s
Low power version of HMOS technology (HCMOS)
32 bit processors
Physical memory space 224 bytes = 16 MB
Virtual memory space 240 bytes = 1 TB
Floating point hardware
Supports increased number of addressing modes
Intel 80386
Fifth Generation Pentium
64 bit processors
History

## Slide 15
It is a 16-bit Microprocessor. So that it has 16 bit ALU, 16 bit registers and internal
data bus and 16 bit external data bus. i.e., It’s ALU, internal registers works on 16-bit
binary word. It make s faster processing.
2. It was implemented in the year 1978 by Intel corp. by using HMOS
(hybrid metal oxide semi-conductor or high speed MOS or high density MOS) technology.
3. 8086 processor has 20 address lines A19-A0, and 16 data lines D15-D0.
8086 has 20 bit address lines to access memory. Hence it can access 220 = 1 MB memory location.
8086 has 16-bit address lines to access I/O devices, hence it can access 216 = 64K I/O location
3. 8086 processor has 20 address lines A19-A0, and 16 data lines D15-D0.
The data lines are multiplexed with lower order 16 address lines, and then
the multiplexed address and data lines areAD15-AD0.
The remaining higher order 4 address lines A16-A19 are multiplexing with the status
Lines S3-S6.
4. It has three versions based on the frequency of operation
a) 8086 : 5MHz b) 8086-2: 8MHz c) 8086-1: 10 MHz
5. 8086 processor is available in 40-pin DIP(Dual in line Package).
Features of 8086: -

## Slide 16
6. 8086 processor supports 256 interrupts.
7. It supports full duplex asynchronous serial communication and half duplex
Synchronous serial communication.
8. 8086 processor have 4 general purpose registers, 4 segment registers,
3 pointer registers, 2 index registers and 1 flag register. (Total : 14 registers)
Size of all these registers is 16-bit.
9. 8086 processor supports segmented version of memory ( 220 =1MB size).
Size of each segment is 64KB. (220 = 24 216 = 24. 64KB= Sixteen 64KB logical segments)
10. 8086 operates in two different modes.
(1) Minimum mode or Single-Processor mode and
(2) Maximum mode or Multi-Processor mode.
Features of 8086: - cont’d…