## Slide 1
Mr. M Krishna Chennakesava Rao,
Asst. Professor, Dept. of ECE,
VFSTR University
Micro Processors & Interfacing
16CS307

## Slide 2
Instruction Format:
Label Field | OPCODE Field | Operand Field | Comment Field
 | OPCODE | Destination Operand , Source operand | 
Next: | ADD | AL, 07H | ; Add 07h to content of AL register

## Slide 3: Addressing Modes of 8086
The different ways in which a processor can access data are called
addressing modes
8086 accesses code bytes using contents of CS & IP register
8086 accesses stack using contents of SS & SP register

## Slide 4
Source of data can be
  Immediate data
  A specified register
  A memory location specified in 1 of many(24) different ways
Destination of data can be
  A specified register
  A memory location specified in 1 of many (24) different ways
Addressing Modes of 8086 cont’d…

## Slide 5
Addressing Modes
An Addressing mode shows how the data is represented in the instruction.
8086 supports 15 addressing modes.
Immediate AM
Register AM
3. Memory Addressing Modes:
i. Direct AM ii. Register Indirect AM iii. Register Relative AM iv. Indexed AM
v. Based Indexed AM vi. Based Indexed Displacement AM
4. Implied AM
I/O AM : a) I/O Direct AM b) I/O Indirect AM
Segment AM :
i. Intra Segment Direct AM ii. Inter Segment Direct AM
iii. Intra Segment Indirect AM iv. Inter Segment Indirect AM

## Slide 6
Addressing Modes
An Addressing mode shows how the data is represented in the instruction.
8086 supports 15 addressing modes.
Immediate AM 2. Register AM
3. Direct AM 4. Register Indirect AM
5. Register Relative AM 6. Based Indexed AM
Based Indexed Displacement AM 8. Implied AM
9. I/O Direct AM 10. I/O Indirect AM
11. Indexed AM 12. Intra Segment Direct AM
13. Inter Segment Direct AM 14. Intra Segment Indirect AM
15. Inter Segment Indirect AM

## Slide 7
Type | Instruction | Source | Address Generation | Destination
Immediate | MOV CH,3AH | Data 3AH |  | Register CH
Register | MOV AX,BX | Register BX |  | Register AX
Direct | MOV [1234H],AX | Register AX | DS*10H + Disp 1000*10H+ 1234 | Memory Address 11234H
Register Indirect | MOV [BX], CL | Register CL | DS*10H + BX 1000*10H+ 0300H | Memory Address 10300H
BX=0300H, SI=0200H, ARRAY=1000H , DS=1000H
Ref: Brey

## Slide 8
Type | Instruction | Source | Address Generation | Destination
Base Index | MOV [BX + SI], BP | Register BP | DS*10H + BX+SI 1000*10H+ 0300H+0200H | Memory Address 10500H
Register Relative | MOV CL, [BX+4] | Memory Address 10304H | DS*10H + BX 1000*10H+ 0300H+4 | Register CL
Base Relative Index | MOV Array[BX + SI], DX | Register DX | DS*10H + Array+ BX+SI 1000*10H+ 1000H+ 0300H+0200H | Memory Address 11500H
BX=0300H, SI=0200H, ARRAY=1000H , DS=1000H

## Slide 9
Type | Instruction | Source | Address Generation | Destination
Scaled Index | MOV [BX +2* SI], AX | Register AX | DS*10H + BX+ 2*SI 1000*10H+ 0300H+0400H | Memory Address 10700H
BX=0300H, SI=0200H, ARRAY=1000H , DS=1000H

## Slide 10
Immediate Addressing Mode: -
The data is directly placed in the source operand field of an instruction.
The immediate data size is either 8bit or 16bit.
The length of the instruction for this AM is either 3byte or 4byte,
if data is moved to register.
Ex: MOV BX, 2050H
If data is moved to a memory location, then the length of instruction is
from 3bytes-6bytes.
Ex: MOV [BX], 2050H
The direct data 2050H will be copied to the Memory location for which
BX gives EA.
Addressing Modes cont’d…

## Slide 11
Addressing Modes cont’d…
Register Addressing Mode: -
Here data is represented in the source operand field, through
a register.
We can use any register except IP.
Length of this AM instruction is 2bytes.
Ex:
MOV AX, BX ; 16-bit data transfer
MOV AL, BL ; 8-bit data transfer

## Slide 12
3. Direct Addressing Mode: -
The address of the data is directly placed in the operand fields
of an instruction.
Here the address of the data is nothing but the memory location address,
i.e, OFFSET or Effective Address.
Ex: MOV AX, [2050]
4. Register Indirect Addressing Mode: -
The address of the data is indirectly represented in operand fields
of the instruction by using registers.
The registers must be BX, BP registers.
Ex: MOV AX, [BX].
Addressing Modes cont’d…

## Slide 13
5. Register Relative Addressing Mode: -
The operand address is provided by the combination of base address
and displacement value.
Ex: MOV AX, 50H[BX]
6. Based Indexed Addressing Mode: -
The operand address is provided by combination of base register
and index register.
Ex: MOV AX, [BX][SI]
Addressing Modes cont’d…

## Slide 14
7. Based Indexed Displacement Addressing Mode: -
The operand address is provided by the combination of base register and
index register and displacement value.
Ex: MOV AX, 50H[BX][SI]
8. Implied Addressing Mode: -
The operand is implicitly represented in operation code of an instruction.
Length of the instruction in this AM is 1byte.
Ex: STD (set DF)
STC (set CF)
Addressing Modes cont’d…

## Slide 15
9. I/O Direct Addressing Mode: -
The I/O device address is directly placed in the operand field of
instruction.
Ex: IN AX, 2050H
OUT 3050H, AL
10. I/O Indirect Addressing Mode: -
The device address placed in operand filed through a register
in the instruction.
Ex: IN AL, [DX]
Addressing Modes cont’d…

## Slide 16
11. Indexed Addressing Mode: -
Here the data address is represented in the operand field through an index register in an instruction.
It is useful when the processor executes string related operations.
It is similar to register indirect AM.
Ex: MOV AX, [SI].
Addressing Modes cont’d…

## Slide 17
12. Intra Segment Direct Addressing Mode: -
If the both source and destination appears in same segment then it is called
intra segment.
The destination address is directly placed in the operand field of the instruction.
Ex: JMP 2050H
13. Inter Segment Direct Addressing Mode: -
If the both source and destination appears in different segment then it is called
inter segment.
The destination address is directly placed in the operand field of the instruction.
Ex: JMP 3000:4050H.
Addressing Modes cont’d…

## Slide 18
14. Intra Segment Indirect Addressing Mode: -
In this AM, the destination address is represented in the operand filed
through a register or a memory location in an instruction.
Ex: JMP word ptr [2050H]
15. Inter Segment Indirect Addressing Mode: -
In this AM, the destination address is represented in the operand filed
through a register or a memory location in an instruction.
Ex: JMP dword ptr [2000H]
Addressing Modes cont’d…