## Slide 1
Mr. M Krishna Chennakesava Rao,
Asst. Professor, Dept. of ECE,
VFSTR University
Micro Processors & Interfacing
16CS307

## Slide 2: Instruction Set of 8086

## Slide 3
Instructions in the instruction set of 8086 are classified into different types,
  Based on number of operand address fields in the instruction.
  Based on type of operation.
Instruction Set of 8086:-

## Slide 4
In this type , instructions can be divided into 3 groups.
1. Zero operand address field Instructions
2. One operand address field Instructions
3. Two operand address field Instructions
Based on Number of Operand Fields in the Instruction
Instruction Set of 8086:- cont’d…

## Slide 5
Zero operand address field instructions
There is no operand fields in the instruction.
Op-code part only exists in the instruction.
Ex:- NOP, HLT, STC, WAIT etc.
2. One operand address field instructions
Only one operand exists in the instruction.
The another operand for the instruction are the default registers (AX or DX)
and these are not represented in the operand field of the instruction.
Ex:- IN AL, OUT AX, DIV BX, and MUL CL etc.
Instruction Set of 8086:- cont’d…

## Slide 6
3. Two operand address field instructions
Both operands are directly represented in the operand fields of instruction.
Ex:- MOV AX,BX
ADD AX, DX
SUB AX, [BP] etc.
Instruction Set of 8086:- cont’d…

## Slide 7
In this type of classification instructions can be divided into 9 groups.
1. Data Transfer instructions 2. Arithmetic Instructions
3. Logical Instructions 4. Shift and Rotate Instructions
5. Branching Instruction 6. Flag Manipulation Instructions
7. Loop Related Instructions 8. Machine Control Instructions
9. String Related Instructions
Instruction Set of 8086:- cont’d…
Based on Type of Operation: -

## Slide 8
Data Transfer instructions are also called as
Data Movement Instructions or
Data Copying Instructions.
If the processor executes any Data Transfer Instruction there is
no effect on the Flag Register Status.
The Data Transfer Instructions are those, which transfers the DATA
(means copy of data) from any one source to any one destination.
The 8086 processor doesn’t support the following types of Data transfer Operations
  Memory to Memory data transfer
  Immediate data to any Segment Register
1. Data Transfer Instructions:-
Instruction Set of 8086:- cont’d…

## Slide 9
General – Purpose Byte or Word Transfer Instructions | Simple Input and Output Port Transfer Instructions | Special Address Transfer Instructions | Flag Transfer Instructions
MOV PUSH POP XCHG XLAT | IN OUT | LEA LDS LES | LAHF SAHF PUSHF POPF
1. Data Transfer Instructions:-
Instruction Set of 8086:- cont’d…

## Slide 10
MOV: - Copy byte or word from specified source to specified destination.
The source operand is either an immediate data or a register or a memory location.
The destination is either a register or a memory location.
Ex: - MOV CX, 037A H
MOV AL, BL
MOVBX, [0301H]
Note: Both source and Destination can’t be memory locations
PUSH: - Copy specified word to top of stack.
The specified word is any 16-bit register content or any memory location contents.
For this instruction execution the content of SP is decrement by ‘2’.
Ex: - PUSH BX
PUSH [1250H]
1. Data Transfer Instructions cont’d…
1.1. General – Purpose Byte or Word Transfer Instructions

## Slide 11
POP: - Copy word form top of stack to specified destination.
Destination can be a general purpose register, segment register (except CS) or
memory location.
For this instruction execution the content of SP is increment by ‘2’.
Ex: - POP CX
POP [2050H]
XCHG: - This instruction exchanges Source with Destination.
It cannot exchange two memory locations directly.
Exchange bytes or exchange words.
Ex: - XCHG DX, AX
XCHG DX, [5040H]
1. Data Transfer Instructions cont’d…
1.1. General – Purpose Byte or Word Transfer Instructions

## Slide 12
XLAT:-Translate a byte using table in the Memory
Replaces a byte AL with a byte in a memory look up table.
BX register stores the starting address of lookup table and
AL register stores OFFSET address
This instruction copies the byte from address pointed by [BX+AL], to AL
1. Data Transfer Instructions cont’d…
1.1. General – Purpose Byte or Word Transfer Instructions

## Slide 13
IN: - Copy a byte or word from specific Input Port to Accumulator.
Ex: - IN AX, 0050H IN Accumulator, I/P Port address
IN AL
OUT: - Copy a byte or word from accumulator to specific Output Port.
Ex: - OUT 0050H, AX OUT O/P Port address, Accumulator
OUT AL
1.2. Input and Output Port Transfer Instructions
1. Data Transfer Instructions cont’d…

## Slide 14
1.3. Address Transfer Instructions
LEA: - Load Effective Address of operand into specified register (16-bit)
LEA Register, source LOCATION
Ex: - LEA BX, [SI]
ii) LDS: - It loads destination register and DS, from memory source.
LDS Register, memory address of first word
The offset is placed in the destination register and the segment base is placed in DS.
To use this instruction the word at the lower order memory address must contain the offset and the word at the higher order address must contain the segment base address.
Ex: - LDS BX, [0302 H]
1. Data Transfer Instructions cont’d…

## Slide 15
LES: - It loads destination register and ES, from memory source.
LES Register, memory address of first word
The offset is placed in the destination register and the segment base is placed in ES.
This instruction is very similar to LDS except that it initializes ES instead of DS.
Ex: - LES DX, [1030 H]
1.3. Address Transfer Instructions
1. Data Transfer Instructions cont’d…

## Slide 16
LAHF: - Load AH with the low byte of flag register. SAHF: - Store AH register to low byte of flag register. PUSHF: - Copy flag register to top of stack. POPF: - Copy word to top of stack to flag register.
1.4. Flag Transfer Instructions
1. Data Transfer Instructions cont’d…

## Slide 17
LAHF:
  It copies the lower byte of flag register to AH.
SAHF:
  It copies the contents of AH to lower byte of flag register.
PUSHF:
  Pushes flag register to top of stack.
POPF:
  Pops the stack top to flag register.
1.4. Flag Transfer Instructions
1. Data Transfer Instructions cont’d…

## Slide 18: Arithmetic Instructions
Addition Instructions | Subtraction Instructions | Multiplication, Increment, & Decrement Instructions | Division Instructions
ADD ADC INC AAA DAA | SUB SBB DEC NEG CMP AAS DAS | MUL IMUL AAM INC DEC | DIV IDIV AAD CBW CWD
To perform Arithmetic calculations
They are classified into four groups.

## Slide 19: Arithmetic Instructions
ADD Des, Src:
  It adds a byte to byte or a word to word.
  It effects AF, CF, OF, PF, SF, ZF flags.
  i.e., All conditional flags will be effected.
  E.g.:
    ADD AL, 74H
    ADD DX, AX
    ADD AX, [BX]

## Slide 20: Arithmetic Instructions
ADC Des, Src:
  It adds the two operands with CF.
  It effects AF, CF, OF, PF, SF, ZF flags.
  i.e., All conditional flags will be effected.
  E.g.:
    ADC AL, 74H
    ADC DX, AX
    ADC AX, [BX]

## Slide 21: Arithmetic Instructions
SUB Des, Src:
  It subtracts a byte from byte or a word from word.
  It effects AF, CF, OF, PF, SF, ZF flags.
  i.e., All conditional flags will be effected.
  For subtraction, CF acts as borrow flag.
  E.g.:
    SUB AL, 74H
    SUB DX, AX
    SUB AX, [BX]

## Slide 22: Arithmetic Instructions
SBB Des, Src:
  It subtracts the two operands and also the borrow from the result.
  It effects AF, CF, OF, PF, SF, ZF flags.
  i.e., All conditional flags will be effected.
  E.g.:
    SBB AL, 74H
    SBB DX, AX
    SBB AX, [BX]

## Slide 23: Arithmetic Instructions
INC Src:
  It increments the byte or word by one.
  The operand can be a register or memory location.
  It effects AF, OF, PF, SF, ZF flags.
  CF is not effected.
  i.e., All conditional flags except CF will be effected.
  Destination operand must not be an immediate number.
  E.g.: INC AX
        INC [BX]
        INC [2050H]

## Slide 24: Arithmetic Instructions
DEC Src:
  It decrements the byte or word by one.
  The operand can be a register or memory location.
  It effects AF, OF, PF, SF, ZF flags.
  CF is not effected.
  i.e., All conditional flags except CF will be effected.
  E.g.: DEC AX
        DEC [BX]
        DEC [2050H]

## Slide 25: Arithmetic Instructions
AAA (ASCII Adjust after Addition):
  The data entered from the terminal is in ASCII format.
  In ASCII, 0 – 9 are represented by 30H – 39H.
  This instruction allows us to add the ASCII codes.
  This instruction does not have any operand.
Other ASCII Instructions:
  AAS (ASCII Adjust after Subtraction)
  AAM (ASCII Adjust after Multiplication)
  AAD (ASCII Adjust Before Division)

## Slide 26: Arithmetic Instructions
DAA (Decimal Adjust after Addition)
  It is used to make sure that the result of adding two BCD numbers is adjusted to be a correct BCD number.
  It only works on AL register.
DAS (Decimal Adjust after Subtraction)
  It is used to make sure that the result of subtracting two BCD numbers is adjusted to be a correct BCD number.
  It only works on AL register.

## Slide 27: Arithmetic Instructions
NEG Src:
  It creates 2’s complement of a given number.
  That means, it changes the sign of a number.
  Ex:
        NEG AX
        NEG [1250H]
        NEG [BX]

## Slide 28: Arithmetic Instructions
CMP Des, Src:
  It compares two specified bytes or words.
  The Src and Des can be a constant, register or memory location.
  Both operands cannot be a memory location at the same time.
  The comparison is done simply by internally subtracting the source from destination.
  The value of source and destination does not change, but the flags are modified to indicate the result.
  Ex:
        CMP AX, BX
        CMP AX, [2050H]
        CMP BX,, 3050H

## Slide 29: Arithmetic Instructions
MUL Src:
  It is an unsigned multiplication instruction.
  It multiplies two bytes to produce a word or two words to produce a double word.
  AX = AL * Src
  DX : AX = AX * Src
  This instruction assumes one of the operand in AL or AX.
  Src can be a register or memory location.
  Ex: MUL BL; MUL [2050H]; MUL CX
IMUL Src:
  It is a signed multiplication instruction.

## Slide 30: Arithmetic Instructions
DIV Src:
  It is an unsigned division instruction.
  It divides word by byte or double word by word.
  The operand is stored in AX, divisor is Src and the result is stored as:
    AH = remainder AL = quotient
    Ex: DIV BL; DIV [2050H]; DIV CX
IDIV Src:
  It is a signed division instruction.

## Slide 31: Arithmetic Instructions
CBW (Convert Byte to Word):
  This instruction converts byte in AL to word in AX.
  The conversion is done by extending the sign bit of AL throughout AH.
  AX = 0000 0000 1001 1000 Convert signed byte in AL signed word in AX Result in AX = 1111 1111 1001 1000
CWD (Convert Word to Double Word):
  This instruction converts word in AX to double word in DX : AX.
  The conversion is done by extending the sign bit of AX throughout DX.
  DX = 1111 1111 1111 1111 Result in AX = 1111 0000 1100 0001

## Slide 32
Logical Instructions
NOT AND OR XOR TEST
3. Logical or Bit Manipulation Instructions

## Slide 33: Bit Manipulation Instructions
These instructions are used at the bit level.
These instructions can be used for:
  Testing a zero bit
  Set or reset a bit
  Shift bits across registers

## Slide 34: Logical or Bit Manipulation Instructions
NOT Src:
  It complements each bit of Src to produce 1’s complement of the specified operand.
  The operand can be a register or memory location.
Ex: - NOT AX
NOT [2050H]

## Slide 35: Bit Manipulation Instructions
AND Des, Src:
  It performs AND operation of Des and Src.
  Src can be immediate number, register or memory location.
  Des can be register or memory location.
  Both operands cannot be memory locations at the same time.
  CF and OF become zero after the operation.
  PF, SF and ZF are updated.
Ex: - AND AX, BX
AND AX, [3050H]
AND AX, 1200H
AND [3040H], 1250H

## Slide 36: Bit Manipulation Instructions
OR Des, Src:
  It performs OR operation of Des and Src.
  Src can be immediate number, register or memory location.
  Des can be register or memory location.
  Both operands cannot be memory locations at the same time.
  CF and OF become zero after the operation.
  PF, SF and ZF are updated.
Ex: - OR AX, BX
OR AX, [3050H]
OR AX, 1200H
OR [3040H], 1250H

## Slide 37: Bit Manipulation Instructions
XOR Des, Src:
  It performs XOR operation of Des and Src.
  Src can be immediate number, register or memory location.
  Des can be register or memory location.
  Both operands cannot be memory locations at the same time.
  CF and OF become zero after the operation.
  PF, SF and ZF are updated.
Ex: - XOR AX, BX
XOR AX, [3050H]
XOR AX, 1200H
XOR [3040H], 1250H

## Slide 38: Bit Manipulation Instructions
TEST Des, Src:
This instruction ANDs the contents of a source byte or word with the contents of specified destination byte or word.
Flags are updated but neither operand is changed .
TEST instruction is often used to set flags before a condition jump instruction.
Ex: - TEST AL, BH; AND BH with AL, updates flags but result not stored.
TEST CX, 0001H

## Slide 39
Shift Instructions | Rotate Instructions
SHL / SAL SHR SAR | ROL ROR RCL RCR
4. Shift and Rotate Instruction
SAL : Shift Arithmetic Left ROL : Rotate Left
SHL: Shift Logical Left RCL: Rotate Left through carry
SAR : Shift Arithmetic Right ROR : Rotate Right
SHR: Shift Logical Right RCR: Rotate Right through carry

## Slide 40: Bit Manipulation Instructions : Shift Instructions
SAL/ SHL Des, Count:
  It shift bits of byte or word to left, by count.
  It puts zero(s) in LSBs. LSB= 0
  MSB is shifted into carry flag. CN=MSB
  If the number of bits desired to be shifted is 1, then the immediate number 1 can be written in Count.
  However, if the number of bits to be shifted is more than 1, then the count is put in CL register. SAL AX,1; MOV CL, 05H; SAL AX, CL
1 | 0 | 1 | 1 | 0 | 1 | 1 | 1
Cy= 0
0
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
Cy= 1

## Slide 41
SHR Des, Count:
  It shift bits of byte or word right, by count.
  It puts zero(s) in MSBs. MSB = 0
  LSB is shifted into carry flag. CN= LSB
  If the number of bits desired to be shifted is 1, then the immediate number 1 can be written in Count.
  However, if the number of bits to be shifted is more than 1, then the count is put in CL register.
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
Cy= 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Cy= 1
0
Bit Manipulation Instructions : Shift Instructions

## Slide 42
SAR Des, Count:
  It shift bits of byte or word right, by count.
  It puts OLD MSB in the new MSB. MSB = OLD MSB
  LSB is shifted into carry flag. CN= LSB
  If the number of bits desired to be shifted is 1, then the immediate number 1 can be written in Count.
  However, if the number of bits to be shifted is more than 1, then the count is put in CL register.
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
Cy= 0
1 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Cy= 1
Bit Manipulation Instructions : Shift Instructions

## Slide 43
ROL Des, Count:
  It rotates bits of byte or word left, by count.
  MSB is transferred to LSB and also to CF. LSB = OLD MSB
  CN= OLD MSB
  If the number of bits desired to be shifted is 1, then the immediate number 1 can be written in Count.
  However, if the number of bits to be shifted is more than 1, then the count is put in CL register.
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1
Cy= 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
Cy= 0
Bit Manipulation Instructions : Rotate Instructions

## Slide 44
ROR Des, Count:
  It rotates bits of byte or word right, by count.
  LSB is transferred to MSB and also to CF.
  MSB= CN= OLD LSB
  If the number of bits desired to be shifted is 1, then the immediate number 1 can be written in Count.
  However, if the number of bits to be shifted is more than 1, then the count is put in CL register.
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
Cy= 0
1 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Cy= 1
Bit Manipulation Instructions : Rotate Instructions

## Slide 45
RCL Des, Count:
  RCL instruction : RCL destination, count
  This instruction rotates all the bits in a specified byte or word some number of bits position to the left along with the carry flags.
  MSB is placed as a new carry and previous carry in place as new LSB. Eg. RCL CX, 1 MOV CL, 04H RCL AL, CL
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1
Cy= 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 1
Cy= 0
Bit Manipulation Instructions : Rotate Instructions

## Slide 46
RCR Des, Count:
  RCR instruction : RCR destination , count
  This instruction rotates all bits in a specified byte or word some number of bit positions to the right along with the carry flag.
  LSB is placed as a new carry and previous carry is in place as a new MSB. Eg. RCR CX, 1 MOV CL, 04H RCR AL, CL
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
Cy= 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Cy= 1
Bit Manipulation Instructions : Rotate Instructions

## Slide 47: 5. Program Flow control Instructions
These instructions cause change in the sequence of the execution of instruction.
This change can be through a condition or sometimes unconditional.
The conditions are represented by flags.
These are also called as Branching Instructions or Transfer of control Instructions.
2 types.
  i. Uncondtional Branching Instructions : CALL RET JMP
  ii. Condtional Branching Instructions : Set of J Cond

## Slide 48: 5.1: Unconditional Branching Instructions
CALL Des: Main  ISR
  This instruction is used to call a subroutine or function or procedure, from a main program.
  Ex: CALL [CX] ; CALL DWORD PTR [BX]
  The address of next instruction after CALL is saved onto stack.
  1. NEAR CALL : is used when the subprogram and main program both appears in same segment
  2. FAR CALL: is used when the subprogram and main program appears in different segments.
  RET: Return from the procedure ISR  Main
  It returns the control from subroutine procedure to calling main program.
  Every CALL instruction should have a RET. It affects no flag.

## Slide 49: 5.1: Unconditional Branching Instructions cont’d.. .
JMP Des:
  This instruction is used for unconditional jump from one place to another. i.e., without taking any condition from conditional flags of 8086.
Ex: - JMP 2000H
JMP [SI]
Jxx Des (Conditional Jump):
  All the conditional jumps follow some conditional statements or any instruction that affects the flag.

## Slide 50: Conditional Jump Table
Mnemonic | Meaning | Jump Condition
JA | Jump if Above | CF = 0 and ZF = 0
JAE | Jump if Above or Equal | CF = 0
JB | Jump if Below | CF = 1
JBE | Jump if Below or Equal | CF = 1 or ZF = 1
JC | Jump if Carry | CF = 1
JE | Jump if Equal | ZF = 1
JNC | Jump if No Carry | CF = 0
JNE | Jump if Not Equal | ZF = 0
JNZ | Jump if Not Zero | ZF = 0
JPE | Jump if Parity is Even | PF = 1
JPO | Jump if Parity is Odd | PF = 0
JZ | Jump if Zero | ZF = 1
5.2: Conditional Branching Instructions

## Slide 51: 6. Loop related Instructions
Loop Des:
  This is a looping instruction.
  The number of times looping is required is placed in the CX register.
  With each iteration, the contents of CX are decremented.
  ZF is checked whether to loop again or not.
  Ex: Loop Unconditional Loop.
  LoopZ / LOOPE Loop through sequence while ZF=1 & CX=0
  LoopNZ / LOOPNE Loop through sequence while ZF=0 & CX=0

## Slide 52: 7. Machine control / Processor Control Instructions
These instructions are used to control the machine operation.
These instructions are also called ‘Processor Control Instructions’.
These instructions control the processor itself.
8086 allows to control certain control flags that:
  causes the processing in a certain direction
  processor synchronization if more than one microprocessor attached.

## Slide 53: 7. Machine control / Processor Control Instructions cont’d…
HLT: - To stop the execution of any ongoing program.
Wait: - To Enter the processor in wait state.
Wait for TEST i/p to go LOW
ESC: Escape
NOP : No Operation
  LOCK : Bus lock prefix

## Slide 54: 8. Flag Manipulation Instructions
STC:
  It Sets the carry flag to 1.
CLC:
  It clears the carry flag to 0.
CMC:
  It complements the carry flag.

## Slide 55: 8. Flag Manipulation Instructions cont’d…
STD:
  It sets the direction flag to 1.
  If it is set, string bytes are accessed from higher memory address to lower memory address. Auto Decrement
CLD:
  It clears the direction flag to 0.
  If it is reset, the string bytes are accessed from lower memory address to higher memory address. Auto Increment
  STI : Set the Interrupt Flag
  CLI : Clear the Interrupt Flag

## Slide 56: 9. String Instructions
String in assembly language is just a sequentially stored bytes or words.
There are very strong set of string instructions in 8086.
By using these string instructions, the size of the program is considerably reduced.
  The length of the string byte must be stored in CX.
The direction flag controls the string instruction execution.
1. If DF=0, execution follows auto increment. (1. CLD)
2. If DF=1, execution follows auto decrement. (2.STD)

## Slide 57: 9. String Instructions cont’d…
3. CMPS Des, Src:
  It compares the string bytes or words.
  The length of the string byte must be stored in CX.
  If both byte or word strings are equal; ZF will SET.
4. SCAS String:
  It scans a string.
  It compares the String with byte in AL or with word in AX.
  Whenever a match to the specified operand, is found in the string, Execution stops and ZF will SET.
  If no match, ZF is RESET.

## Slide 58: 9. String Instructions cont’d…
5. MOVS / MOVSB / MOVSW:
  It causes moving of byte or word from one string to another.
  The length of the string byte must be stored in CX.
  In this instruction, the source string is in Data Segment and destination string is in Extra Segment.
  SI and DI store the offset values for source and destination index.
  String copies as following.
  DS : SI  ES : DI

## Slide 59: 9. String Instructions cont’d…
6. REP (Repeat):
  This is an instruction prefix.
  It causes the repetition of the instruction until CX becomes zero.
  E.g.: REP MOVSB STR1, STR2
    It copies byte by byte contents.
    REP repeats the operation MOVSB until CX becomes zero.

## Slide 60: 9. String Instructions cont’d…
7. LODS : Load String byte or word:
It loads AL/ AX register by a string pointed by DS: SI
DS  AL
8. STOS: Store string byte or word:
It stores AL/ AX register content to a string pointed by ES: DI
AL  DS

## Slide 61
Queries ?