## Slide 1
Mr. M Krishna Chennakesava Rao,
Asst. Professor, Dept. of ECE,
VFSTR University
Micro Processors & Interfacing
16CS307

## Slide 2
Bit Addition
MOV AX,[2100]
MOV BX,[2102]
ADD AX,BX
MOV [2140],AX
INT 03
HLT
16 Bit Subtraction
MOV AX,[2100]
MOV BX,[2102]
SUB AX,BX
MOV [2140],AX
INT 03
HLT
16 Bit Multiplication
MOV AX,[0500]
MOV BX,[0502]
MUL BX
INT 03
HLT
16BIT DIVISION
MOV AX,000CH
MOV BL,04H
DIV BL
INT 03
HLT
Multi Byte ADDITION
MOV CX,000A
MOV BX,0500
MOV SI,0600
MOV DI,0700
L1: MOV AX,[BX]
ADC AX,[SI]
MOV [DI],AX
INC BX
INC SI
INC DI
LOOP L1
INT 03
HLT
Simple Programs using 8086 Microprocessor

## Slide 3
LARGEST NO IN AN ARRAY
MOV SI,0300
MOV CL, 06
MOV AL,00
L1: CMP AL,[SI]
JAE L2
MOV AL,[SI]
L2: INC SI
LOOP L1
MOV [SI],AX
INT 03
HLT
 | AL | CL= 06 | CL= 05 | CL= 04 | CL= 03 | CL= 02 | CL= 01 | CL= 00
 | E9 | 13 | 13 | 13 | 13 | 13 | 13 | 13
 | E9 | 13 | 13 | 13 | 13 | 13 | 13 | 13
 | E9 | 68 | 68 | 68 | 68 | 68 | 68 | 68
 | B4 | E9 | E9 | E9 | E9 | E9 | E9 | E9
 | B4 | 4A | 4A | 4A | 4A | 4A | 4A | 4A
 | 35 | B4 | B4 | B4 | B4 | B4 | B4 | B4
SI 0300 | 00 | 35 | 35 | 35 | 35 | 35 | 35 | 35

## Slide 4
LARGEST NO IN AN ARRAY
MOV SI,0300
MOV CX,0006
MOV AX,0000
L1: CMP AX,[SI]
JAE L2
MOV AX,[SI]
L2: INC SI
INC SI
LOOP NE L1
MOV [SI],AX
INT 03
HLT
 | AL | CX=06 |  |  |  |  |  | 
 |  | 13 | 13 | 13 | 13 | 13 | 13 | 13
 |  | 68 | 68 | 68 | 68 | 68 | 68 | 68
 |  | E9 | E9 | E9 | E9 | E9 | E9 | E9
 |  | 4A | 4A | 4A | 4A | 4A | 4A | 4A
SI 0301 |  | B4 | B4 | B4 | B4 | B4 | B4 | B4
SI 0300 |  | 35 | 35 | 35 | 35 | 35 | 35 | 35

## Slide 5
SMALLEST NUMBER IN AN ARRAY
MOV SI,0300
MOV CX,0003
MOV AX,FFFF
L1 : CMP AX,[SI]
JB L2
MOV AX,[SI]
L2 : INC SI
INC SI
LOOP NE L1
MOV [SI],AX
INT 03
HLT

## Slide 6
AM OF N NO’S
MOV BX,0500
MOV CL,[BX]
MOV DI,0000
INC BX
L1: MOV AL,[BX]
MOV AH,00
ADD DI, AX
INC BX
LOOP L1
MOV DL,[0500]
MOV AX,DI
DIV DL
INT 03
HLT

## Slide 7
SUM OF SQUARES OF ‘N’
NATURAL NUMBERS
MOV CX,[3000]
MOV BX,0001
L1: MOV AX,BX
MUL AX
ADD [3002],AX
INC BX
DEC CX
JNZ L1
INT 03
HLT
SUM OF CUBES OF N
NATURAL NO’S
MOV CX,[3000]
MOV BX,0001
L1: MOV AX,BX
MUL AX
MUL BX
ADD [3002],AX
INC BX
DEC CX
JNZ L1
INT 03
HLT
SUM OF N NATURAL NO’S
MOV AX,0005
MOV BX,AX
INC BX
MUL BX
MOV CL,02
DIV CL
INT 03
HLT
Hint: n(n+1)/2

## Slide 8
ASCENDING ORDER
MOV CX,0000
MOV DL,04
L3: MOV DI,0500
MOV CL,DL
MOV BX,0500
MOV AL,[BX]
L2: INC BX
CMP AL,[BX]
JNC L1
MOV AL,[BX]
MOV DI,BX
L1: DEC CX
JNZ L2
MOV AH,[BX]
MOV [BX],AL
MOV [DI],AH
DEC DL
JNZ L3
INT 03
HLT
DESCENDING ORDER
MOV CX,0000
MOV DL,04
L3: MOV DI,0500
MOV CL,DL
MOV BX.0500
MOV AL,[BX]
L2: INC BX
CMP AL,[BX]
JC L1
MOV AL,[BX]
MOV DI,BX
L1: DEC CX
JNZ L2
MOV AH,[BX]
MOV [BX],AL
MOV [DI],AH
DEC DL
JNZ L3
INT 03
HLT

## Slide 9
Multi Byte Addition
Assume CS:CODE,DS:DATA
CODE SEGMENT
MOV AX,DATA
MOV DS,AX
LEA SI,NUM1
LEA DI,NUM2
LEA BX,RESULT
MOV CX,0004 H
L1: MOV AL,[SI]
ADC AL,[DI]
MOV [BX],AL
INC SI
INC DI
INC BX
LOOP L1
INT 03
CODE ENDS
DATA SEGMENT
NUM1 DB 04H DUP(0)
NUM2 DB 04H DUP(0)
RESULT DB 04H DUP(0)
DATA ENDS
END